## Slide 1
EG1003: Introduction to Engineering and Design
Electronic Filters

## Slide 2: Overview
Objectives
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3: Objectives
Learn about electrical filters
  Different types
  Uses
What is the -3dB point?
Create filters and a crystal set radio using multiple circuit elements
Identify filters based on generated graphs

## Slide 4: Frequency Response Graph
Gain (in dB)
  Ratio of output against input
  20*log (Vout/Vin)
  Always negative value
-3dB Point
  3dB drop of signal power from highest point on gain
  Signal power is half of original value
Cutoff Frequency (in Hz)
  Frequency at -3dB Point

## Slide 5: Frequency Response Graph
Plot of Gain versus Frequency of electrical signal
Semi-logarithmic scale
  Linear Y-axis, logarithmic X-axis
Cutoff Frequency
3 dB
f (kHz) (log scale)
Gain (dB)
(linear scale)
Gain vs. Frequency
Max Gain (dB)
Gain is 3 dB lower than the max
Bandwidth

## Slide 6: What are Filters?
Eliminate unwanted frequencies
  High-pass or low-pass
Favor desired frequencies
  Band-pass
    Bandwidth: frequency range filter allows to pass
Example
    Radio tunes in to particular station

## Slide 7: Basic Filter Types
Low-Pass Filter
  Low frequencies pass
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequency:
1590 Hz
Bandwidth: 0 - 1590 Hz
PASS
IGNORE

## Slide 8: Basic Filter Types
High-Pass Filter
  High frequencies pass
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequency:
160 Hz
Bandwidth: 160 - ∞ Hz
PASS
IGNORE

## Slide 9: Basic Filter Types
Band-Pass Filter
  Limited frequency range passes
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequencies:
400 and 600 Hz
Bandwidth: 400 - 600 Hz
Resonant Frequency (High Response Point):
500 Hz
PASS
IGNORE
IGNORE

## Slide 10: Electrical Terminology
Voltage (V) [unit = V for Volts]
  Potential difference in electrical energy
Current (I) [unit = A for Amperes]
  Charge flow rate
  Can be positive or negative
Terms
Elements
Wiring

## Slide 11: Electrical Terminology
Resistor (R)
[unit = Ω for Ohms]
  Resists flow of electrical current
  Dissipates electrical energy as heat
  Often used to alter voltages in circuits
  Characterized by Ohm’s Law: V = I*R
  Not sensitive to frequency
  Uses a poor conductor
    Example: Carbon
Terms
Elements
Wiring
Symbol

## Slide 12: Electrical Terminology
Capacitor (C) [unit = F for Farads]
  Stores potential energy (V)
  Affected by voltage and frequency
  A pair metal plates separated by non-conductive material
    Example: Air
  Electrical charge accumulates on plates
Terms
Elements
Wiring
Symbol

## Slide 13: Electrical Terminology
Inductor (L) [unit = H for Henries]
  Stores and delivers energy in a magnetic field
  Magnetic fields affect the current of a circuit
  Effected by current and frequency
  Is a coil of wire
Terms
Elements
Wiring
Symbol
Notes: Needs to be fixed

## Slide 14: Electrical Terminology
Series
  Same current through
  all elements
  Vin = VA + VB + VC
Parallel
  Same voltage across
  all branches
  Vin = VD = VE = VF + VG
Terms
Elements
Wiring

## Slide 15: Materials for Lab
Resistors
  Brown, black, yellow = 100KΩ
  Brown, black, green = 1MΩ
Capacitors
  102 = 0.001 µF
  10J = 10pF
Inductors
  1mH

## Slide 16: Materials for Lab (Cont’d)
NI-ELVIS II+
Breadboard
Coaxial to Alligator Clip Cable

## Slide 17: Procedure - Testing
  Plug in NI ELVIS II to PC Lab and turn it on
  Select NI ELVISmx Instrument Launcher
  Select FGEN in the Instrument Launcher
  Set function generator to 1000Hz
  Set the amplitude to 2 Vpp
  Set signal route to FGEN BNC
  Select Scope in the Instrument Launcher

## Slide 18: Procedure – Data Analysis
Click run in both instruments
Calculate the -3dB point
Test both of the circuits and determine their type
Assemble the radio

## Slide 19: Procedure - Circuit 1
Connect the 100kΩ resistor and .001 µF capacitor in series

## Slide 20: Procedure - Circuit 2
Connect 0.001 µF capacitor to 1 MΩ resistor in series

## Slide 21: Procedure - Circuit 3
Assemble the circuit below (Crystal Radio)

## Slide 22: Assignment: Report
Individual Report (one report per student)
Title page
Discussion topics in the manual
For first two circuits
  Include Excel tables and Gain vs. Frequency graphs
  Determine filter type
  Label each graph with determined filter type
Have TA scan in signed lab notes
OPTIONAL- Include photos of circuits and setup

## Slide 23: Assignment: Presentation
Team Presentation
Include lab data
Professional-looking tables
Discussion topics in the manual
Include photos of circuits and setup
Refer to “Creating PowerPoint Presentations” found in Online Manual

## Slide 24: Closing
TA will assign which circuit you start with
Have all original data signed by your TA
All team members must actively participate in experiment
Submit all work electronically
Return all materials to your TA