## Slide 1
EG1003: Introduction to Engineering and Design
Electronic Filters

## Slide 2
Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3
Objective
Learn about electrical filters
Different types
Uses
What is the -3dB point?
Create filters and a crystal set radio using multiple circuit elements
Identify filters based on generated graphs

## Slide 4
Frequency Response Graph
Gain (in dB)
Ratio of output against input
20*log (Vout/Vin)
Always negative value
-3dB Point
3dB drop of signal power from highest point on gain
Signal power is half of original value
Cutoff Frequency (in Hz)
Frequency at -3dB Point

## Slide 5
Frequency Response Graph
Plot of Gain versus Frequency of electrical signal
Semi-logarithmic scale
Linear Y-axis, logarithmic X-axis
Cutoff Frequency
3 dB
f (kHz) (log scale)
Gain (dB)
(linear scale)
Gain vs. Frequency
Max Gain (dB)
Gain is 3 dB lower than the max
Bandwidth

## Slide 6
What are Filters?
Eliminate unwanted frequencies
High-pass or low-pass
Favor desired frequencies
Band-pass
Bandwidth: frequency range filter allows to pass
Example
Radio tunes in to particular station

## Slide 7
Basic Filter Types
Low-Pass Filter
  Low frequencies pass
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequency:
1590 Hz
Bandwidth: 0 - 1590 Hz
IGNORE
PASS

## Slide 8
Basic Filter Types
High-Pass Filter
High frequencies pass
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequency:
160 Hz
Bandwidth: 160 - ∞ Hz
PASS
IGNORE

## Slide 9
Basic Filter Types
Band-Pass Filter
Limited frequency range passes
Low-Pass
High-Pass
Band-Pass
3dB Point: -3dB
Cutoff Frequencies:
400 and 600 Hz
Bandwidth: 400 - 600 Hz
Resonant Freq (High Response Pt):500 Hz
IGNORE
IGNORE
PASS

## Slide 10
Electrical Terminology
Voltage (V) [unit = V for Volts]
Potential difference in electrical energy
Current (I) [unit = A for Amperes]
Charge flow rate
Can be positive or negative
Terms
Elements
Wiring

## Slide 11
Electrical Terminology
Resistor (R)
[unit = Ω for Ohms]
Resists flow of electrical current
Dissipates electrical energy as heat
Often used to alter voltages in circuits
Characterized by Ohm’s Law: V = I*R
Not sensitive to frequency
Uses a poor conductor
Example: Carbon
Terms
Elements
Wiring
Symbol

## Slide 12
Electrical Terminology
Capacitor (C) [unit = F for Farads]
Stores potential energy (V)
Affected by voltage and frequency
A pair metal plates separated by non-conductive material
Example: Air
Electrical charge accumulates on plates
Terms
Elements
Wiring
Symbol

## Slide 13
Electrical Terminology
Inductor (L) [unit = H for Henries]
Stores and delivers energy in a magnetic field
Magnetic fields affect the current of a circuit
Effected by current and frequency
Is a coil of wire
Terms
Elements
Wiring
Symbol

## Slide 14
Electrical Terminology
Series
Same current through all elements
Vin = VA + VB + VC
Parallel
Same voltage across all branches
Vin = VD = VE = VF + VG
Terms
Elements
Wiring

## Slide 15
Materials
Resistors
Brown, black, yellow = 100KΩ
Brown, black, green = 1MΩ
Capacitors
102 = 0.001 µF
10J = 10pF
Inductors
1mH

## Slide 16
Materials (Cont’d)
NI-ELVIS II+
Breadboard
Coaxial to Alligator Clip Cable

## Slide 17
Procedure - Testing
Plug in NI ELVIS II to PC Lab and turn it on
Select NI ELVISmx Instrument Launcher
Select FGEN in the Instrument Launcher
Set function generator to 1000Hz
Set the amplitude to 2 Vpp
Set signal route to FGEN BNC
Select Scope in the Instrument Launcher

## Slide 18
Procedure – Data Analysis
Click run in both instruments
Calculate the -3dB point
Test both of the circuits and determine their type
Assemble the radio

## Slide 19
Procedure - Circuit 1
Connect the 100kΩ resistor and .001 µF capacitor in series

## Slide 20
Procedure - Circuit 2
Connect 0.001 µF capacitor to 1 MΩ resistor in series

## Slide 21
Assignment: Presentation
Assemble the circuit below (Crystal Radio)

## Slide 22
Assignment: Report
Individual Report (one report per student)
Title page
Discussion topics in the manual
For all circuits
Include Excel tables and Gain vs. Frequency graphs
Determine filter type
Label each graph with determined filter type
OPTIONAL- Include photos of circuits and setup

## Slide 23
Assignment: Presentation
Team Presentation
Include lab data
Professional-looking tables
Discussion topics in the manual
Include photos of circuits and setup
Refer to “Creating PowerPoint Presentations” found in Online Manual

## Slide 24
Closing
TA will assign which circuit you start with
Have all original data signed by your TA
All team members must actively participate in experiment
Submit all work electronically
Return all materials to your TA