## Slide 1: Heat Transfer & Thermal Insulation
Notes: L.Mexhitaj 2009

## Slide 2: Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3: Objectives
Design and construct container to minimize heat loss from an egg within
Understand concept of minimal design
Understand :
  thermodynamic systems
  temperature
  heat and heat transfer
Notes: Thermodynamic Systems, Temperature added

## Slide 4: Thermodynamic Systems
Part of the universe separated from the surroundings by a boundary (real or imaginary)
3 types of systems:
  Open system: exchange energy and matter
  Closed system: exchange energy
  Isolated system: no exchange
Notes: New Slide: Paul-Henry Volmar – September 2007

## Slide 5: Temperature
Qualitative laymen perception:
  hot, warm, cold…
Physical property of system:
  Average kinetic energy of
  atoms and/or molecules
  Absolute zero occurs when
  average kinetic energy is
  zero: 0oK
Notes: Temperature slide added - Paul-Henry Volmar – September 2007-

## Slide 6: Heat & Heat Transfer
Heat: thermal energy (total kinetic energy of all atoms and/or molecules)
Heat transfer: passage of thermal energy from hot to cold body
Can NEVER be stopped, only SLOWED DOWN
Notes: Modified Heat Transfer Slide

## Slide 7: Equilibrium
Equilibrium reached
  Temperature at all points in a system are equal
65o
73o
125o
50o
39o
25o
80o
95o
90o
58o
Initial State
70
70o
70o
70o
70o
70o
70o
70o
70o
70o
Final State

## Slide 8: Means of Heat Transfer
Three types of heat transfer covered:
  Conduction: through matter (solids)
  Convection: through fluids
  Radiation: does not require medium

## Slide 9: Conduction
100°F
200°F
Heat transferred through a solid body
k = Coefficient of
thermal conductivity
A = Cross-sectional area
q = Heat transferred per unit time
Δ T = Difference in
temperature
Δ X = Length of material

## Slide 10: Example of Conduction
Atoms are heated and begin to vibrate
Vibrating atoms hit adjacent atoms, increasing temperature
Heat travels atom to atom up to the end of the rod

## Slide 11: Convection
Heat transferred by mass transport of atoms
Heat transfer between solid and fluid
(liquid or gas)
Two types of convection
Iron
Water
h = coefficient of
convection
A =cross-sectional area
q =Heat transferred per unit time
Δ T = difference in
temperature

## Slide 12: Types of Convection
Natural Convection
  Density of fluid changes with temperature
  Fluids expand as temperature rises and decrease density
  Buoyant forces dominate
Forced Convection or Advection
  Fluid flow caused by a device or environment
  More heat transfer than natural convection
  Buoyancy has little effect on direction of flow

## Slide 13: Example of Natural Convection
Atoms move around and are heated by fire
Warm air rises
(less dense)
Transfers energy to adjacent (air) molecules
Warm air cools, becomes more dense, and sinks
Process repeats

## Slide 14: Radiation
Energy exchanged between bodies in form of electromagnetic waves
Can travel through a vacuum
(requires no medium)
q = heat transferred per unit time Ts = surface temperature (absolute)
e = constant of emissivity T∞ = surrounding temperature (absolute)
A = surface area σ= Stefan-Boltzmann’s constant
Notes: Radiation picture added – Paul-Henry Volmar – September 2007

## Slide 15: Thermal Insulation
Slows down heat transfer
Examples:
  Clothing
  Walls of houses
  Refrigerators
  Thermos bottles

## Slide 16: Minimal Design
Minimal design - ability to design an object that is both functional and economical
  Goal 1: Maximize functionality
  Goal 2: Minimize cost

## Slide 17: Materials For This Lab
Foam chips
Plastic wrap
Tape
Aluminum foil
Cup
  Styrofoam
  Paper
Plastic cup lid
Boiled egg
Thermocouple and wire connectors
Thermal LabVIEW program
DAC board

## Slide 18: Problem Statement
Design/construct insulating container to accept hot egg just removed from boiling water
Container should minimize heat loss from egg
Use minimal design concepts

## Slide 19: Material Price List
Large foam cup………………………$0.50
Lid…………………………………………$0.25
Paper cup……………………………… $0.40
Styrofoam pieces.………………… $0.05 / 6
Tape …………………………………… $0.10/ ft
Aluminum foil ……………………… $0.30/ ft2
Plastic wrap ………………………..$0.02 / ft2

## Slide 20: Rules of the Competition
All materials must remain inside chosen container
Container cannot be larger than largest cup provided
No external heat sources may be used
Start LabVIEW program when container cover is closed and egg is inside
Container may not be held or covered during temperature readings
Egg may not be returned to water (No “restarts”)
At least one cup must be used
Egg shell may not be cracked
Container must remain on surface of testing area
Thermocouple must only be taped to surface of egg shell
Design Specs.
Disqualifications
Declaration of winners

## Slide 21: Rules of the Competition
Disqualifications occur when:
Any materials are outside the container
Container is held during testing
Any external heating source is used
Testing not started within 30 seconds of receiving egg
Design Specs.
Disqualifications
Declaration of winners

## Slide 22: Rules of the Competition
IC = insulating capability of container
IC is slope of last 5 minutes of heat loss plot
TR is room temperature, TF is final thermocouple temperature
Team with lowest Minimal Design Ratio wins
Extra points for TA lab report
  Winning team +10
  2nd place team +5 (4 or more teams)
  3rd place team +2 (8 or more teams)
Design Specs.
Disqualifications
Declaration of winners

## Slide 23: Procedure
Pre-Test
Observe provided materials
Brainstorm for possible designs
Sketch design on paper
  Label properly
Construct design according to your sketch
  Note design changes
Create price list detailing your design
Pre-Test
Test
Post-Test

## Slide 24: Procedure
Test
  * TA performs test using an unmodified cup (control experiment)
  Receive boiled egg from instructor
  Tape one end of thermocouple wire to egg (constant contact essential)
  Insert egg with attached thermocouple
  Quickly close container
  Start LabVIEW program
Pre-Test
Test
Post-Test

## Slide 25: Procedure
Post-Test
LabVIEW program has run for 15 minutes
  Excel table automatically created after test
Use data on table to create Excel graph of Temperature vs. Time
Show table and graph to TA
  TA will initial lab notes that table and graph have been created
Save table and graph
Have photo taken of container
Pre-Test
Test
Post-Test

## Slide 26: Assignment: Report
Individual BONUS (!) Report
Title page
Discussion topics in the manual
Include original data with instructor’s initials
Scan in lab notes (ask TA for assistance)
  TA must initial that table and graph were completed
Include table, graph, and photo of container

## Slide 27: Assignment: Presentation
Team presentation
State rules of competition
Describe your design and its concepts
Explain steps taken to complete lab
Professional-looking tables and graph
How could your current design be improved?
Refer to “Creating PowerPoint Presentations” found on EG website

## Slide 28: Closing
Have all original data signed by TA
Each team member should have turn using software
Submit all work electronically
Return all unused materials to TA
Discard egg after testing