## Slide 1: Laboratory 7: Sensors
Notes: Matthew R. Gaglio, Feb 2007

## Slide 2: Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3: Objectives
Design two sensor programs
  Mindstorms: use sensors to stop a motor when a red ball is detected
  LabVIEW: use a thermocouple to measure temperature in a heating and cooling program
Apply sensors to Semester-Long Design Projects

## Slide 4: Concept : Control Systems
Control system
  System created to read and analyze data
  Use analyzed data for appropriate action
  Examples:
    Thermal controls
    Lighting systems
    Alarm systems
    Motion sensors

## Slide 5: Concept: Sensors
Sensors
  Read data from test environment
  Data converted to digital format for computer
Some sensor types:
  Light
  Temperature
  Ultrasonic
  Touch
Sensors connect to different control devices:
  Lego sensors -> NXT
  Thermocouple -> DAC -> PC

## Slide 6: Materials
Mindstorms sensor program
  NXT
  Test assembly
  Computer with Mindstorms
LabVIEW sensor program
  Computer with LabVIEW + DAC
  Thermocouple

## Slide 7: Procedure: Mindstorms Sensor Program Part A
Port 1 touch sensor
  Starts program
  Starts motor on Port A
  Reverses direction of motor
Port 2 touch sensor
  Stops motor on Port A
  Ends program
Port B motor
  Varies speed of Port A motor

## Slide 8: Procedure: Mindstorms Sensor Program Part B
Port 3 ultrasonic sensor
  Reverse direction of motor when greater than 20cm from wall
  Reverse direction of motor when less than 8cm from wall

## Slide 9: Procedure: Mindstorms Sensor Program Part C
Port 4 light sensor
  Stops motor when red ball is detected
  (value greater than 45)
  Ends program

## Slide 10: Procedure: LabVIEW Sensor Program
Design (based on VI from LabVIEW Lab)
  Back Panel – Add “AI Sample Channel.vi”
    Name the channel “thermocouple”
      Receives input from thermocouple
    Change thermometer to indicator
      Display input
Testing and Data
  Insert thermocouple wires
    Yellow wire -> Pin 3 of DAC
    Orange wire -> Pin 4 of DAC
  Have TA test your program
  Take screenshot of Front and Back Panels

## Slide 11: Assignment: Report/Presentation
No report for this lab
No Presentation for this lab
Milestone 2 due next recitation

## Slide 12: Closing
Have all lab notes signed by TA
Each team member should have turn using software
Return all unused materials to TA