## Slide 1: LAZ & MRR WORKSHOP
EG1003 | LAB 4A

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Assignment
Closing
1
Figure 1: VEX Robotics Logo Courtesy of VEX Robotics

## Slide 3: OBJECTIVE
Program a small VEX robot to navigate a mini-course
Become familiar with the Arduino VEX library
Understand when and how to use a gyro sensor
2

## Slide 4: BACKGROUND INFORMATION
VEX Robotics
  Used for LAZ and MRR projects
  Educational robotic system
  Microcontroller, motor shield, motors, battery, gyro sensor
Figure 2: VEX Clawbot Courtesy of Robot Mesh
3

## Slide 5: BACKGROUND INFORMATION
Figure 3: Arduino Microcontroller Layout
Figure 4: Arduino Motor Shield Layout
Figure 5: Gyro Sensor
4

## Slide 6: BACKGROUND INFORMATION
Figure 6: Motors and Battery Wiring
5
Figure 7: Gyro Wiring

## Slide 7: BACKGROUND INFORMATION
Arduino IDE – program to edit, compile, and upload code to the Arduino board
Code written in the Arduino programming language (based on C/C++)
VEX Library
6
Figure 8: Arduino IDE

## Slide 8: BACKGROUND INFORMATION
Order of Code:
  Import VEX Library
  Declare Object(s)
    Objects in the VEX Library include
      Vex Object
      Motor Objects
      Sensor Objects
  Call object functions to program the VEX Robot
    Each object type has different programmable functions that relate to their physical functions.
    Example: Robot.moveTank()
7
Figure 9: Example of Code in Arduino
1
2
3

## Slide 9: BACKGROUND INFORMATION
8
Sensor | Description | Picture
Gyro | Tracks the angle that the robot is turning or positioned at. | 
Ultrasonic | Determines how far the robot is from an obstacle. (returns the total distance) | 
Touch | Determines whether the robot is pressing against and obstacle or edge of the course. | 
IRObstacle | Detects if there are obstacles in the robot’s path. (returns HIGH if there’s an obstacle and LOW if there isn’t) | 

## Slide 10: MATERIALS
A lab PC
Pre-built mini VEX robot
Mini VEX Course
Gyro Sensor
Arduino
9
Figure 10: Mini VEX robot

## Slide 11: PROCEDURE
Part 1: Importing the Library
  Download and import the VEX Library into Arduino
Part 2: Setting up the VEX Robot Object
  Coding the robot to move forward
  Traverse tiles 1-4
Part 3: Setting up the Gyro Sensor Object
  Use gyro sensor to turn the robot
  Traverse tiles 4-5
Extra: Complete the Entire Course
  Traverse tiles 5-8
10
Figure 11: Mini VEX Robot

## Slide 12: PROCEDURE
11
Figure 12: Mini VEX Course

## Slide 13: ASSIGNMENT
No lab report
No team presentation
12

## Slide 14: CLOSING
Ask TAs for help if needed
Only finish the entire course if time allows
Be careful not to go full power
Do not let any two exposed wires touch
Do not unplug the gyros or remove the motor shield
Disconnect the VEX battery when not in use
13
Figure 13: VEX Battery Courtesy of VEX Robotics

## Slide 15
Starting next week will run twice a week
2 Sessions per topic
Held in Modelshop (JAB 573)
14
TECHNICAL WORKSHOPS

## Slide 16
February |  |  |  |  |  | 
Sun | Mon | Tue | Wed | Thr | Fri | Sat
 |  | 1 | 2 | 3 | 4 | 5
6 | 7 | 8 | 9 | 10 | 11 | 12
13 | 14 | 15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24 | 25 | 26
27 | 28 |  |  |  |  | 
CAD, Ideation & Manufacturing
2/23 Wednesday 7-8pm
2/27 Sunday 2-3pm
15

## Slide 17
March |  |  |  |  |  | 
Sun | Mon | Tue | Wed | Thr | Fri | Sat
 |  | 1 | 2 | 3 | 4 | 5
6 | 7 | 8 | 9 | 10 | 11 | 12
13 | 14 | 15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24 | 25 | 26
27 | 28 | 29 | 30 | 31 | 1 | 2
Arduino
3/2 Wednesday 7-8pm
3/13 Sunday 2-3pm
Raspberry Pi
3/6 Sunday 2-3pm
3/9 Wednesday 7-8pm
Circuitry
3/16 Wednesday 7-8pm
3/27 Sunday 2-3pm
Revit
3/20 Sunday 2-3pm
3/23 Wednesday 7-8pm
Soldering
3/30 Wednesday 7-8pm
4/3 Sunday 2-3pm
16