## Slide 1: SUSTAINABLE ENERGY VEHICLE
EG1003 | LAB 5

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Assignment
Closing
1
Figure 1: Renewable Energy Sources Courtesy of Physics World

## Slide 3: OBJECTIVE
To evaluate energy storage devices
To evaluate different sources of renewable energy
To design a sustainable energy vehicle to enter in a competition
2

## Slide 4: BACKGROUND INFORMATION
Renewable energy – energy harnessed from naturally replenished resources
Figure 2: Renewable vs. Non-Renewable Energy Sources Courtesy of Solar Schools
3

## Slide 5: BACKGROUND INFORMATION
Solar panels – convert sunlight to electrical energy
  Incident sunlight excites electrons to next energy level, emitting energy
  Usually made of silicon
Figure 3: How Solar Panels Work Courtesy of Good Energy
4

## Slide 6: BACKGROUND INFORMATION
Wind turbine – converts wind energy to electrical energy
  Wind causes pressure difference on turbine blades
  Utilizes gear ratios to power generator
Figure 4: How Wind Turbines Work
Courtesy of Tech-Addict
5
Notes: Rotating blades turn a low-speed shaft to a gearbox, which outputs power to an electrical generator through a high-speed shaft.

## Slide 7: BACKGROUND INFORMATION
Capacitor – stores charge temporarily
  Are polarized
  Charged logarithmically (initially charges very fast but rate of charging slows down)
Figure 5: Polarized Leads of 1 Farad Capacitor
6
Positive
Negative

## Slide 8: BACKGROUND INFORMATION
Symbols for common electrical components:
  Battery
  Capacitor
  DC source
7
  Voltmeter
  Ammeter

## Slide 9: BACKGROUND INFORMATION
Series circuit
  Current is equal across components
  Voltage across each component:
8
Parallel circuit
  Current varies across components
  Voltage across each component:
Figure 6: Series Circuit
Figure 7: Parallel Circuit

## Slide 10: BACKGROUND INFORMATION
Digital multimeter – reads current and voltage across circuits
  Measure current in series, called ammeter
  Measure voltage in parallel, called voltmeter
9
Figure 8: Circuits for Using a Multimeter

## Slide 11: BACKGROUND INFORMATION
VEX Robotics – educational robotics kit used to design interactive robots
Commonly used to model capabilities of vehicles
Will be used to model sustainable energy vehicle design in Fusion 360
10
Figure 9: VEX Clawbot (Left) and VEX Motor (Right)
Courtesy of Robot Mesh

## Slide 12: MATERIALS
Horizon wind-turbine
Sunforce 50013 1 W solar battery charger
Adjustable table fan
Heat lamp
3V power supply
Digital multimeter
Music voltmeter
1 F 5.5V capacitor
3 alligator clip sets
Virtual VEX Kit
11

## Slide 13: PROCEDURE
12
Remote students will complete some of Part 1 and 2 on TinkerCAD
Part 1: Test the power storage device
  Charge a capacitor (In-Person & Remote)
Part 2: Test the assigned power source using music voltmeter/multimeter
  Solar panel (In-Person)
  Wind turbine (In-Person)
  Lemon battery (Remote)
  Potato battery (Remote)
  Data Analysis (Hybrid)

## Slide 14: PROCEDURE
13
Part 3: Design a sustainable energy vehicle using the power source of choice in Fusion 360 (Hybrid)
  Extra Credit Use Sweep to create wires that connects the capacitors to the motors
Figure 10: Simple VEX Robot courtesy of Chris and Jim CIM

## Slide 15: PROCEDURE
Vehicle Design Rules:
The sustainable energy vehicle must carry the capacitors
Two motors are allowed
Modify the design to have a location to store the power storage device
The motors must be connected to a minimum of two wheels
14

## Slide 16: ASSIGNMENT
15
Optional extra credit individual lab report:
  Answer discussion questions in manual
  Include picture and explanation of vehicle design
  Include spreadsheet with power source data
  Include pictures and screenshots of all circuits
  Due at 11:59 PM the night before Lab 6
Team presentation:
  Address discussion points in manual

## Slide 17: CLOSING
16
Measure current in series and voltage in parallel
Submit all work electronically
Take screenshots of the vehicle design
Clean up workstations
Return all unused materials to the TA

## Slide 18: QUESTIONS?