## Slide 1
INTRODUCTION TO DIGITAL LOGIC
LAB 5
EG 1004 Introduction to Engineering & Design

## Slide 2
OVERVIEW
Objective
Background Information
Materials
Procedure
Competition Rules
IDBE Implementation
Assignment
Closing
Figure 1: Semiconductor Courtesy of Scoop.it

## Slide 3
OBJECTIVE
To design a combinational logic circuit for a given problem statement
To build and test the circuit on a breadboard

## Slide 4
BACKGROUND
Digital logic
  Conceptual language behind modern computer systems
  Two values of true and false (1 and 0) that lead to complicated decisions
Figure 2: Boolean Circuit Courtesy of All About Circuits
Shows all the possible input combinations and their associated outputs
(example on next slide)
Truth Table
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 5
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 6
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 7
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 8
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 9
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 10
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 11
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 12
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 13
BACKGROUND
Table 1: Truth Table for ATM Example
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 14
BACKGROUND
Both inputs must be true for the output to be true
AND gate
Inverts the input
NOT gate
If either input is true, the output will be true
OR gate
Logic Gates
Table 2: Logic Gates
 | NOT | AND | OR
Symbol |  |  | 
Arithmetic Operation |  |  | 
# of Inputs | 1 | 2+ | 2+
 | NOT | AND | OR
Symbol |  |  | 
Arithmetic Operation |  |  | 
# of Inputs | 1 | 2+ | 2+
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 15
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 16
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 17
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 18
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 19
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 20
BACKGROUND
Table 3: Truth Table for ATM Example with True Combinations
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Mathematical representation of all the combinations in the truth table that yield an output of 1
Boolean Equation
Represents when a fee is charged in the ATM example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 21
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 22
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 23
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 24
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 25
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 26
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 27
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 |  |  | 
 | 0 |  |  | 
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 28
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 |  |  | 
 | 0 |  |  | 
 | 0 |  |  | 
 | 0 |  |  | 
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 29
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 |  | 
 | 0 |  |  | 
 | 0 | 1 |  | 
 | 0 |  |  | 
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 30
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 |  | 
 | 0 | 1 |  | 
 | 0 | 1 |  | 
 | 0 | 1 |  | 
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 31
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 |  | 1
 | 0 | 1 |  | 
 | 0 | 1 |  | 1
 | 0 | 1 |  | 
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 32
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 |  | 1
 | 0 | 1 |  | 0
 | 0 | 1 |  | 1
 | 0 | 1 |  | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 33
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 | 1 | 1
 | 0 | 1 |  | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 |  | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 34
BACKGROUND
Two-dimensional representation that shows the common characteristics of the inputs
Only one value can change t a time between adjacent rows and columns
Karnaugh Map (K-map)
Table 4: K-map for ATM Example
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 35
BACKGROUND
Mathematical representation of true values in the K-map
  Box together 1s in the K-map
  Number of cells in a box must be a power of 2 (1, 2, 4, 8, etc.)
  Look for the biggest boxes first
  Boxes can overlap
Simplified equation is determined by constant variable(s) in each box
Simplified Boolean Equation
Table 5: Simplified Boolean Equation for ATM Example
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 36
BACKGROUND
Mathematical representation of true values in the K-map
  Box together 1s in the K-map
  Number of cells in a box must be a power of 2 (1, 2, 4, 8, etc.)
  Look for the biggest boxes first
  Boxes can overlap
Simplified equation is determined by constant variable(s) in each box
Simplified Boolean Equation
Table 5: Simplified Boolean Equation for ATM Example
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 37
BACKGROUND
Mathematical representation of true values in the K-map
  Box together 1s in the K-map
  Number of cells in a box must be a power of 2 (1, 2, 4, 8, etc.)
  Look for the biggest boxes first
  Boxes can overlap
Simplified equation is determined by constant variable(s) in each box
Simplified Boolean Equation
Table 5: Simplified Boolean Equation for ATM Example
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 38
BACKGROUND
Combinational Logic Circuit – graphical representation of the simplified Boolean equation
NOT
AND
OR
Figure 3: Combinational Logic Circuit for ATM Example
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 39
BACKGROUND
Minimization of Boolean functions
  K-map used to simplify complex Boolean equations
  Reduces complexity of logic circuit
  Would increase efficiency and decrease cost in implementation
Figure 4: Complex Logic Circuit (Left) vs.
Simplified Logic Circuit (Right)
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 40
BACKGROUND
Chips that consist of small assemblies of electronic components
Integrated Circuits (ICs)
Logic Gate ICs consist of logic gates that can be used to prototype combinational logic circuits on a breadboard
Figure 5: Diagram of NOT/AND/OR IC Chips
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 41
BACKGROUND
Figure 6: Diagram of the example ATM circuit
Print (P)
Withdraw (W)
Deposit (D)
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 42
A 7432 IC (4 dual-input OR gates)
A 7408 IC (4 dual-input AND gates)
A 7404 IC (6 single-input NOT gates)
Breadboard
5V Battery Case
LED
220 Ω Resistor
Slide Switches
Wires
MATERIALS
Figure 7: Integrated circuit (IC) chips courtesy of Wikipedia

## Slide 43
PROBLEM STATEMENT
Farmer Georgi has a hen on his 350-acre farm that produces high-quality eggs
To protect the hen from a fox who has been wandering around the farm and his grain, he needs an alarm system
Figure 8: Farmer Georgi’s Farm Courtesy of ThoughtCo

## Slide 44
PROBLEM STATEMENT
Farmer Georgi has two barns
  Think of Barn A as “0” and Barn B as “1” in the truth table
A fox, hen, and grain can be in either barn at anytime
Design an alarm system that will sound when:
  The fox and hen are in the same barn
  The hen and grain are in the same barn

## Slide 45
Part I: Formulate the Simplified Boolean Equation
Build a truth table for the alarm system
Create a Boolean equation
Build a K-map
Create a simplified Boolean equation
Draw a combinational logic circuit
  Add a light bulb to represent the alarm
PROCEDURE
Figure 9: IC Chip

## Slide 46
Part II: Test the IC Chips
Use the Arduino board setup by the TAs to test the NOT/OR/AND IC chips
The Arduino program will determine if the IC chips are functional or not
Orient the IC chips properly
PROCEDURE
Figure 10: IC chip tester

## Slide 47
Part III: Build the Combinational Logic Circuit
Build and test the logic circuit on a breadboard
  Wire the combinational logic circuit using the IC chips
  Power (+5V) and ground the IC chips
  Orient the IC chips properly
PROCEDURE
Figure 11: Diagram of NOT/AND/OR IC Chips

## Slide 48
IDBE IMPLEMENTATION
Accessible Designs
  Designing an alarm with flashing lights is better for deaf users
  Reduces noise pollution
  But for visually impaired users, noise alarms are necessary
Be Aware– flashing lights and loud noises can have adverse effects on different people
As socially-aware engineers, what alarm solutions can you think of?
Figure 12: Flashing Fire Alarm
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 49
ASSIGNMENT
Team lab report:
  Answer discussion questions in manual
  Explain how k-maps help simplify the circuitry
  Include the truth table, both Boolean equations, and k-map
  Include pictures of the completed logic circuit
  Due at 11:59 PM the night before Lab 6
Team presentation:
  Address discussion points in manual
  Include pictures of the completed logic circuit
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 50
CLOSING
Take pictures of the completed logic circuit
Clean up workstations
Return all unused materials to the TA
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 51
QUESTIONS?