## Slide 1: COMPUTER-AIDED DESIGN (CAD) COMPETITION
EG1003 | LAB 2

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Competition Rules
Assignment
Closing
1
Figure 1: Fusion 360 (Left) and Cura (Right) Courtesy of AppRecs and Wikipedia

## Slide 3: OBJECTIVE
Use CAD software, Fusion 360, to design a keychain
Analyze and modify a poorly-designed part in Fusion 360
Enter the modified part in a competition against other redesigns
2

## Slide 4: BACKGROUND
Fusion 360
  Computer-Aided Design (CAD) software
  Creates 3D drawings of engineering designs
  Also used for CAM, rendering, simulation, etc.
3D printing – allows for rapid prototyping and onsite manufacturing
Cura
  3D printing preparation application
6
Figure 2: Fusion 360 in use courtesy of Autodesk

## Slide 5: BACKGROUND INFORMATION
Design workspace
  Used to make precisely-scaled drawings of engineering designs
  Sketch a 2D profile
  Generate 3D body using Extrude, Sweep, or Loft
Figure 3: Extrude and Sweep tools
4

## Slide 6: BACKGROUND INFORMATION
Loft
  Creates a 3D extrusion to connect two profiles
Sweep
  Creates a 3D model of a surface (profile) along a specific path
Figure 3: Extrude and Sweep tools
4
Notes: The video has NO AUDIO, so make sure to walk through and narrate what is happening. The first thing they do here is a loft, and then a sweep.

## Slide 7: BACKGROUND INFORMATION
Simulation workspace
  Used to run structural analysis on model under real-world conditions
  Define the constraints (boundary conditions) on the model
  Apply a load to simulate real-world force
  Generate a mesh, an array of polygons making up the body of the model
Figure 4: Fusion 360 mesh courtesy of O’Reilly
5

## Slide 8: BACKGROUND INFORMATION
Simulation workspace
  Run simulation to obtain safety factor, a value used to describe how much stronger a system is than the expected load
  Can determine if an object is ready to sustain real-world loads or needs to be remodified
Figure 5: Fusion 360 simulation courtesy of Engineering.com
6

## Slide 9: MATERIALS
A lab PC
Fusion 360
Predesigned part files (download directly from the manual)
8
Figure 6: Truss Pyramid

## Slide 10: PROCEDURE
Part 1: Set up the File
Part 2: Design a Keychain
  Use the manual tutorial to create an NYU keychain
10
Figure 7: NYU Keychain to Design

## Slide 11: PROCEDURE
Part 3: CAD Competition
  Find the load, material, and constraints on the model
  Run a static stress simulation
  Review the initial factor of safety
  Modify the model in the Design workspace within the limits of the competition rules
  Rerun simulations and remodify until the part has safety factor of at least 3
  Save and store the F3D file for later use
9
Figure 8: Screwed bracket static stress simulation

## Slide 12: COMPETITION RULES
Redesigned part must be less than double the initial volume
Redesigned part must have a safety factor of at least 3
Cannot alter the applied loads or constraints
Cannot alter the areas highlighted in red on the model
10
Figure 9: Wire Supported Shelf

## Slide 13: ASSIGNMENT
Individual lab report:
  Answer discussion questions in manual
  Keychain section need not be discussed
  Include screenshots of at least two simulations
  Due at 11:59 PM the night before Lab 3
Team presentation:
  Address discussion points in manual
  Keychain section need not be discussed
  Include drawings (top, front, most detailed side, isometric) of unmodified and modified part
  Due at 11:59 PM the night before Recitation 3
13

## Slide 14: CLOSING
Have all original data signed by a TA
Submit all work electronically
Take screenshots of mechanical part before and after modification
15

## Slide 15: QUESTIONS?