## Slide 1: EG1004 Laboratory 9: Lemon-Powered Car
Notes: Fall 2006 Pratima G.

## Slide 2: Overview
Experimental Objective
Background Information
Materials
Procedure
Report / Presentation
Conclusion

## Slide 3: Experimental Objective
Determine potency of reducing agents
Create chemical cells to generate electricity
Use capacitors to store/release energy
Build car powered by chemical reaction

## Slide 4: Background Information
Fundamental ideas
Redox (reduction/oxidation) reactions
Batteries
Designing citrus cell batteries
Capacitors

## Slide 5: Fundamental Ideas
Electronegativity: measure of element’s attractions of another’s electrons
Ionization energy: energy to remove electron from atom and form a cation
Both properties
Increase:
left to right
bottom to top
Periodic Table

## Slide 6: Redox Reactions
When a reaction can be separated into oxidation and reduction
Oxidation: electron loss
ex: Mg  Mg+2 + 2e-
Reduction: electron gain
ex: O2 + 4e-  2O-2
Notes: Oil Rig is a analogy for this property (Oxidation Is Loss, Reduction Is Gain)

## Slide 7: Batteries
Battery arrangement
  Series circuit increases voltage
  Parallel circuit increases current

## Slide 8: Capacitors
Store electrical energy
1Farad Polarized Capacitor
Positive
Negative

## Slide 9: Capacitor Charging
Capacitor charge limit is restricted by charge voltage
Maximizing applied voltage maximizes energy stored
Capacitor is charged in time increments called the time constant (tau):
τ =RC
R=resistance C=capacitance

## Slide 10: Percentage Charged
Charge is logarithmic
It takes approximately 4τ to charge the capacitor
Ex:

## Slide 11: Designing of Citrus Cells
A citrus cell/battery
  Uses two different electrodes
  Citrus acid used as electrolyte

## Slide 12: Electrolytic Solutions
Non-metallic part of circuit
Electrolytes dissociate free ions to create an electrically conductive solution
Lemon Juice used as electrolyte

## Slide 13: Materials
Lemons
Lemon Juice
Magnesium
Copper
Zinc
Nickel
Aluminum
3 Alligator Cable Sets
1 Farad 2.5v Capacitor
Standard Lego Car Chassis
Lego to Alligator Cable Clip Connector
Light Emitting Diode (LED)
Small Cups
Scissors
Tape
DMM (Digital Multi-meter)
Large Plates

## Slide 14: Procedure
Part 1
  Determine voltage potential of electrodes
  Determine positive and negative poles
Part 2
  Light up LED using two lemon cells with most potent electrode pairs
Part 3
  Decide on the power source
    Chemical cell or capacitor
  Design/Build your car to accept power source

## Slide 15: Procedure
Part 1
  Acquire Materials
  Squeeze/roll lemon
  Insert electrodes into lemon ½ cm from each other
  Connect electrodes to DMM
    Record Voltage
    Determine polarity of lemon cell

## Slide 16: Procedure
Part 2
  Create second citrus cell
  Connect two citrus cells in series
    Attach to LED
    Is it lit?

## Slide 17: Procedure
Part 3
  Choose your electrodes (remember cost)
  Design your power source
    Chemical or capacitor
  Design car for power source
    Allow 15 min for capacitor to charge
  Create a sketch/pricelist
  TA must sign your work
  Enter competition
Notes: N

## Slide 18: Competition
Factors that will effect the CR (Competition Ratio) are:
  Distance traveled in 60 seconds
  Cost of components
Item | Cost
Capacitor | $1.00
2oz Lemon Juice (with cup) | $0.25
1.5" Mg Strips | $1.00
Cu Strip | $0.25
Zn Strip | $0.50
Al Strip | $0.25
Ni Strip | $0.25
Lemon Car Components | $0.00
Cost List

## Slide 19: Assignment: Report
Team report
Title page
Discussion topics in the manual
Include original data with instructor’s initials
  Scan in data and lab notes
  (ask TA for assistance)

## Slide 20: Assignment: Presentation
Team presentation
Include photos of the lemon car
Explain how the battery works

## Slide 21: Conclusion
Return all electrodes to TA
  Have return signed
Clean up all materials
TAs will tabulate competition results
Extra credit awarded according to manual