## Slide 1
EG1003: Introduction to Engineering and Design
Introduction to LabVIEW

## Slide 2
Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3
Objective
Familiarization with graphical programming
Obtain data from outside the computer using simulated instrumentation
Use this knowledge to create programs in LabVIEW
Simple calculator
Heating and cooling system
Lighting system

## Slide 4
What is LabVIEW?
Laboratory Virtual Instrument Engineering Workbench
Graphical programming language
Used for data acquisition, instrument control, and signal processing
Based on G programming language

## Slide 5
Text-based

## Slide 6
Graphic-based

## Slide 7
LabVIEW Programs (VIs)
Called “Virtual Instruments” (VIs)
Appearance and operation imitates actual physical instruments
Without
With

## Slide 8
Applications in EG1003
Heat Transfer and Thermal Insulation Lab
Temperature Recording
Electronic Filters Lab
Oscilloscope (SignalExpress)
Semester Long Project – Supermarket, Train
Lighting system and heater/AC
Security system
Light sensors
Switches rail paths

## Slide 9
LabVIEW Interface
Front Panel - User Interface (UI), where the program is controlled and executed
Back Panel (Block Diagram) - The internal circuit where the program code is written

## Slide 10
Controls and Indicators
Icon in back panel represents object in front panel

## Slide 11
Color Representation

## Slide 12
LabVIEW Tools

## Slide 13
LabVIEW Functions (View > Functions)

## Slide 14
Structures
Allow programmer to produce conditional statements or multiple outputs, based on input
Example
Case Structure
Executes code based
on input value

## Slide 15
NI-ELVIS Board
National Instruments’ Educational Laboratory Virtual Instrumentation Suite Board
Interface that exchanges data (sends/receives) between the computer and the outside world
References: See EG1003 Online Manual, National Instruments documentation, and other LabVIEW oriented websites (i.e. IIT’s LabVIEW for Dummies©)

## Slide 16
Pattern and Pin activation
Activate multiple pins
Use compound arithmetic operator
Add as many inputs as needed
Click and drag the bottom to add inputs
Link sum to Build Array

## Slide 17
Materials
Computer with LabVIEW
NI-ELVIS Board
Wires

## Slide 18
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 1: Simple Calculator VI
  Create program simulating basic calculator
  Able to add, subtract, and multiply

## Slide 19
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 1: Simple Calculator VI
Front panel of program must have:
  1 slide to control 3 different arithmetic operations (add +; subtract -; multiply *)
  3 LED (Boolean) indicators to show which arithmetic operation is selected
  Two numeric controls for inputting numbers
  One numeric indicator to display results
  Back panel should have:
  A case statement to control arithmetic operations

## Slide 20
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 2: Thermal Control VI
  Home heating/cooling system
  Program requirements- Automatic Mode
  Regulate house air temperature
  AC is ON when temperature is greater than 80oF
  Heater is ON when the temperature is less than 60oF
  Heater and AC are OFF when temperature is between 60oF and 80oF
  Program requirements- Manual Mode
  Heater and AC power are controlled directly by user (overrides automatic mode)

## Slide 21
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 2: Thermal Control VI
  Front panel must have:
  3 LEDs
  AC on/off indicator
  Heater on/off indicator
  Manual operation on/off indicator
  3 switches for AC, heater and system operation (automatic/manual)
  A temperature control represented by a thermometer
  Back panel should have:
  A Boolean case statement to control manual and automatic operations

## Slide 22
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 3: Lighting System VI
  Simulate typical household lighting system
  Use Boolean indicators in conjunction with real LEDs to illustrate operation

## Slide 23
Procedure
Program 1: Simple Calculator
Program 2: Thermal Control
Program 3: Lighting System
Program 3: Lighting System VI
Front panel must have:
Main power on/off switch for all lights
4 lights, each representing a different room
Each light should have a separate on/off switch
Back panel should have:
A “NI ELVISmx Digital Writer node” setup to control LEDs through board
A Boolean case for each LED
Real world
Functional LED assembly (depict real lights)

## Slide 24
Assignment: Report/Presentation
Submit a Zip file with all LabVIEW programs (.vi)
No Presentation for this Lab
Individual report
Title page
Discussion topics in the manual
Scan in data and lab notes (ask TA for assistance)

## Slide 25
Closing
Have all lab notes signed by TA
Each team member should have turn using software
Save Heating and Cooling VI – to be used in a future lab session
Submit all work electronically
Return all unused materials to TA