## Slide 1: Introduction to LabVIEW

## Slide 2
Overview
Objectives
Background
Materials
Procedure
Report/Presentation
Closing

## Slide 3
Objective
Familiarization with graphical programming
Obtain data from outside the computer using simulated instrumentation
Use this knowledge to create programs in LabVIEW
  Simple calculator
  Lighting system
  Heating and cooling system

## Slide 4
What is LabVIEW?
Laboratory Virtual Instrument Engineering Workbench
Graphical programming language
Used for data acquisition, instrument control, and signal processing
Based on G programming language

## Slide 5
Text-Based
Text-based code for a simple calculator

## Slide 6
Graphic-Based
Graphic-based code for a simple calculator

## Slide 7
LabVIEW Programs (VIs)
Called “Virtual Instruments” (VIs)
Appearance and operation imitates actual physical instruments
Without
With

## Slide 8
Applications in EG1003
Heat Transfer and Thermal Insulation Lab
  Temperature recording
Electronic Filters Lab
  Oscilloscope (SingalExpress)
Semester Long Design Project – Supermarket, Train
  Lighting system and heater/AC
  Security system
  Light sensors
  Switches rail paths

## Slide 9
Graphic-Based
Back Panel (Block Diagram): The internal circuit where the program code is written
Front Panel - User Interface (UI), where the program is controlled and executed

## Slide 10
Controls and Indicators
Icons in back panel represent objects in front panel
Controls can be identified by a triangle on the right of the block shown on the back panel

## Slide 11
Toolbar & Tools Panel
Run once
Run Continuously
Stop
Pause
Highlight Execution
Automatic Tool Selector
Operating Tool
Positioning Tool
Labeling Tool
Wiring Tool
Scrolling Tool
Probe Tool
Coloring Tool
Get Color

## Slide 12
LabVIEW Functions (View > Functions)
The Functions palette contains the VIs, functions and constants you use to create the block diagram.
Only items highlighted in red will be covered in this course

## Slide 13
NI-ELVIS Board
National Instruments’ Educational Laboratory Virtual Instrumentation Suite Board
Interface that exchanges data (sends/receives) between the computer and the outside world
  References: See EG1003 Online Manual, National Instruments documentation, and other LabVIEW oriented websites (i.e. IIT’s LabVIEW for Dummies©)

## Slide 14
Pattern and Pin Activation
Activate multiple pins
Use compound arithmetic operator
Add as many inputs as needs
Click and drag the bottom to add inputs
Link sum to Build Array

## Slide 15
Materials
Computer with LabVIEW
NI-ELVIS board
Wires
3D-Printed Heat Cube

## Slide 16
Procedure
Program 1 (Simple Calculator VI)
Create program simulating basic calculator
Able to add, subtract, and multiply

## Slide 17
Procedure
Front panel of program must have:
  1 slide to control 3 different arithmetic operations (add +, subtract -, multiply *)
  3 LED (Boolean) indicators to show which arithmetic operation is selected
  Two numeric controls for inputting numbers
  One numeric indicator to display results
Back panel must have:
  A case statement to control arithmetic operations

## Slide 18
Procedure
Program 2 (Lighting System VI)
Simulate typical household lighting system
Use Boolean indicators in conjunction with real LEDs to illustrate operation

## Slide 19
Procedure
Front panel must have:
  Main power on/off switch for all lights
  4 lights, each representing a different room
  Each light should have a separate on/off switch
Back panel should have:
  A “NI ELVISmx Digital Writer node” setup to control LEDs through board
  A Boolean case for each LED
Real world: functional LED assembly depict real lights

## Slide 20
Procedure
Program 3 (Thermal Control VI)
Program requirements – Automatic Mode
  Regulate house air temperature
  AC is ON when temperature is greater than 80oF
  Heater is ON when temperature is less than 60oF
  Both OFF when the temperature is between 60oF & 80oF
Program requirements – Manual Mode
  Heater and AC power are controlled directly by user (overrides automatic mode)

## Slide 21
Procedure
Front panel must have:
  3 LEDs: AC, Heater, and Manual operation
  3 switches for AC, heater, and system operation (automatic/manual)
  A temperature control represented by a thermometer
Back panel should have:
  A Boolean case statement to control manual and automatic operations

## Slide 22
Procedure
Real World
Functional heating/cooling system “Heat Cube”
Import premade VIs to control fans, heaters, and thermometers using your logic program
  Temperature Reading VI: receive real time data
  Heat Control VI: power heating element
  Cooling Control VI: power fan/cooling unit

## Slide 23
Report/Presentation
Submit a Zip file with all LabVIEW programs (.vi)
No presentation for this lab
Individual report
Discussion topics in the manual
Scan in data and lab notes

## Slide 24
Closing
Have all lab notes signed by TA
Each team member should have turn using software
Save Heating and Cooling VI
Submit all work electronically
Return all unused materials to TA

## Slide 25
Introduction to LabVIEW
QUESTIONS?