## Slide 1
EG1003: Introduction to Engineering and Design
Digital Logic Circuits

## Slide 2
Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3
Objective
Understand logic gates and digital logic circuits
Design combinational logic circuit
Activate under specific conditions
Test with LabVIEW
Test using NI-ELVIS prototyping board

## Slide 4
Logic Functions
AND - “All or nothing operator”
Output high (1) only when ALL inputs are high (1)
OR gate - “Any or all operator”
Output high (1) when at least ONE input is high (1)
NOT operator – “Inverter”
Output always opposite of input
Only one input and one output

## Slide 5
Logic Functions
Logic Function | Logic Symbol | Boolean Expression | Truth Table |  | 
 |  |  | Inputs |  | Output
 |  |  | A | B | Y
AND |  | A • B = Y | 0 | 0 | 0
 |  |  | 0 | 1 | 0
 |  |  | 1 | 0 | 0
 |  |  | 1 | 1 | 1
OR |  | A + B = Y | 0 | 0 | 0
 |  |  | 0 | 1 | 1
 |  |  | 1 | 0 | 1
 |  |  | 1 | 1 | 1
NOT |  | A = Ā | 0 | - | 1
 |  |  | 1 | - | 0

## Slide 6
Sample Problem
ATM machine has three options:
Print statement
Withdraw money
Deposit money
ATM machine will charge $1.00 to:
Withdraw
Print out statement with no transactions
No charge for:
Deposits without withdrawal

## Slide 7
Competition Rules
A truth table displays all possible input / output combinations.
INPUT OUTPUT
P = Print C = Charge
W = Withdraw
D = Deposit
0 = “do not” 0 = $0.00
1 = “do” 1 = $1.00
INPUTS
OUTPUT
P
W
D
C
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 8
INPUTS
OUTPUT
P
W
D
C
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
C =
PWD
+ PWD
+ PWD
+ PWD
+ PWD
Outputs with a value of “ONE” are kept
Boolean Equations

## Slide 9
W
C = PWD+ PWD+ PWD + PWD + PWD
P
P
P
P
W
W
W
D
D
1
1
1
1
1
_
Why can’t you switch PW and PW?
0
1
Why can’t you loop the three
adjacent 1s in the top row together?
PWD
PWD
PWD
0
0
1
1
1
1
0
0
0
0
0
Karnaugh Maps (K-maps)

## Slide 10
Karnaugh Maps (K-maps)
W
P
P
P
P
W
W
W
D
D
1
1
1
1
1
0
0
0
1
1
1
1
0
0
1
NOTE:Circle neighboring ONES in powers of 2. Try to find the greatest amount of “neighbors.” Only overlap circles as a last resort!
0
0
0
C = PWD+ PWD+ PWD + PWD + PWD

## Slide 11
1
1
_ _
PWD
1
1
_
PWD
_
PWD
PWD
C =
W
Opposite values cancel out
1
1
_
PWD
_ _
PWD
P
P
P
P
W
W
W
W
D
D
1
1
1
1
1
_
+ PD
0
0
0
Simplified Boolean Equation

## Slide 12
_
PWD
1
1
1
1
1
C = W + PD
P
P
P
P
W
W
W
W
D
D
Opposite values in circles cancel out
_ _
PWD
PWD
_
PWD
_
PWD
= W
3
Step 1
2
4
_
PWD
_ _
PWD
_
= PD
Step 1
0
0
0
Simplified Boolean Equation

## Slide 13
W
P
D
_
D
_
PD
C =
W
P
D
+
W
P
D
P
D
+
W
P
D
+
W
P
D
+
Combinational Logic Circuit

## Slide 14
Integrated Circuits (ICs)
Used for implementation of combinational logic circuits
Use TTL family (transistor transistor logic)

## Slide 15
IC Identification

## Slide 16
Materials for Lab
Computer equipped with LabVIEW
NI-ELVIS II+ Prototyping Board
DIP Switch
Hook-up Wire

## Slide 17
Problem Statement
A farmer has 2 barns
3 items: fox, hen, corn
Items can be in any barn, in any combination
Concerns:
Protect hen from fox
Protect corn from hen
Design alarm system using digital electronics. Alarm sounds when:
Fox and hen are in same barn
Hen and corn are in same barn

## Slide 18
Problem Statement
Design combination logic circuit for alarm system:
Use least amount of gates and input variables (cost effectiveness)
Logical circuit output connected to LED
LED “on” indicates alarm activation
LED “off” indicates no problem (alarm off)
Fox, hen and corn must be in barn 1 or barn 2
Presence in barn 1 = 1
Presence in barn 2 = 0

## Slide 19
Procedure
Truth Table
Determine input and output variable (s)
How many combinations are there?
Complete truth table on a sheet of paper
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 20
Procedure
Boolean Expression
Gather all combinations that produce a 1 for output
Create a Boolean expression from these smaller expressions (independent conditions)
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 21
Procedure
K-Map
Create a K-Map table
Only have one variable change state at a time between adjacent boxes
Use the Boolean expression to fill in the 1’s
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 22
Procedure
Simplified Boolean Expression
Use K-Map to circle groups of 1’s
1’s may only be circled in powers of 2, starting from largest possible combination and working downward
Write new simplified expression
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 23
Procedure
Logic Circuit Diagram
Use new simplified Boolean expression to design a logic circuit
Have TA check/initial work
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 24
Procedure
LabVIEW Simulation
Create logic circuit in LabVIEW based on theoretical work
Front panel
3 control switches represent input variables
1 Boolean indicator shows output
HINT: some LabVIEW comparison functions are:
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS
NOT
AND
OR

## Slide 25
Procedure
NI-ELVIS Prototyping Board
Do NOT electrically connect anything until TA has reviewed your work
Connect +5V and ground to the DIP switch
Use created logic circuit and IC chip diagram to wire actual circuit on the prototyping board
Be sure to connect each of the ICs to “Ground” and “+5V” (circuit power)
Connect final output to an LED.
**VCC is an acronym:
**Voltage at the Common Collector (+5V)
Truth Table
Boolean Expression
K-Map
Simplified Boolean Expression
Logic Circuit
LabVIEW Simulation
NI-ELVIS

## Slide 26
Assignment: Report
Individual Report
Title page
Discussion topics in the manual
Scan in data and lab notes
Original tables and work should be legible
Include screenshots of LabVIEW front and back panels

## Slide 27
Assignment: Presentation
Team presentation
Professional-looking tables
Include screen shots of your programs
Photo of functioning LED assembly
Explain steps taken to complete lab
Be prepared to provide walk-through
Include lab data
Refer to “Creating PowerPoint Presentations” found in Online Manual

## Slide 28
Closing
Have all original data signed by TA
Each team member should have turn using software
Submit all work electronically
Return all unused materials to TA