## Slide 1: Digital Logic Circuits

## Slide 2
Overview
Objectives
Background
Materials
Procedure
Report/Presentation
Closing

## Slide 3
Objective
Understand logic gates and digital logic circuits
Design combinational logic circuit
  Activate under specific conditions
  Test with LabVIEW
  Test using NI-ELVIS prototyping board

## Slide 4
Logic Functions
AND - “All or nothing operator”
  Output high (1) only when ALL inputs are high (1)
  OR gate - “Any or all operator”
  Output high (1) when at least ONE input is high (1)
  NOT operator – “Inverter”
  Output always opposite of input
  Only one input and one output

## Slide 5
Logic Functions
Logic Function | Logic Symbol | Boolean Expression | Truth Table |  | 
 |  |  | Inputs |  | Output
 |  |  | A | B | Y
AND |  | A • B = Y | 0 | 0 | 0
 |  |  | 0 | 1 | 0
 |  |  | 1 | 0 | 0
 |  |  | 1 | 1 | 1
OR |  | A + B = Y | 0 | 0 | 0
 |  |  | 0 | 1 | 1
 |  |  | 1 | 0 | 1
 |  |  | 1 | 1 | 1
NOT |  | A = Ā | 0 | - | 1
 |  |  | 1 | - | 0

## Slide 6
Sample Problem
ATM machine has three options:
  Print statement
  Withdraw money
  Deposit money
ATM machine will charge $1.00 to:
  Withdraw
  Print out statement with no transactions
No charge for: Deposits without withdrawal

## Slide 7
Sample Problem
A truth table displays all possible input / output combinations. | 
INPUTS | OUTPUT
P = Print W= Withdraw D = Deposit | C = Charge
0 = “do not” 1 = “do” | 0 = $0.00 1 = $1.00

## Slide 8
Sample Problem
Outputs with a value of “ONE” are kept
C = PWD
+ PWD
+ PWD
+ PWD
+ PWD

## Slide 9
Sample Problem
Karnaugh Maps (K-maps)
C = PWD + PWD + PWD+ PWD + PWD
NOTE: Circle neighboring ONES in powers of 2. (Ex: 2, 4, 8 etc.)
Try to find the greatest amount of “neighbors.”
Only overlap circles as a last resort!
 | PW | PW | PW | PW
D | 0 | 1 | 1 | 1
D | 0 | 1 | 1 | 0

## Slide 10
Sample Problem
C = PWD + PWD + PWD+ PWD + PWD
 | PW | PW | PW | PW
D | 0 | 1 | 1 | 1
D | 0 | 1 | 1 | 0
Grouped terms share variables in common (Ex. W is common in the bigger group)
The uncommon terms in a group can be eliminated to simplify the previous equation
C= W + PD

## Slide 11
Sample Problem
W
P
D
_
D
_
PD
C =
W
P
D
+
W
P
D
P
D
+
W
P
D
+
W
P
D
+
Implementation of logic

## Slide 12
Integrated Circuits (ICs)
Used for implementation of combinational logic circuits
  Use TTL family (transistor transistor logic)

## Slide 13
IC Identification

## Slide 14
Materials
Computer equipped with LabVIEW
NI-ELVIS II+ Prototyping Board
Prototyping Wire and IC Chips

## Slide 15
Problem Statement
A farmer has 2 barns
  3 items: fox, hen, corn
    Items can be in any barn, in any combination
  Concerns:
    Protect hen from fox
    Protect corn from hen
Design alarm system using digital electronics that sounds when:
  Fox and hen are in same barn
  Hen and corn are in same barn

## Slide 16
Problem Statement
Design combination logic circuit for alarm system:
  Use least amount of gates and input variables (cost effectiveness)
Logical circuit output connected to LED
  LED “on” indicates alarm activation
  LED “off” indicates no problem (alarm off)
Fox, hen and corn must be in barn 1 or barn 2
  Presence in barn 1 = 1
  Presence in barn 2 = 0

## Slide 17
Procedure
Truth Table
Determine input and output variable (s)
How many combinations are there?
Complete truth table on a sheet of paper

## Slide 18
Procedure
Boolean Expression
Gather all combinations that produce a 1 for output
Create a Boolean expression from these smaller expressions (independent conditions)

## Slide 19
Procedure
K-Map
Create a K-Map table
Only have one variable change state at a time between adjacent boxes
Use the Boolean expression to fill in the 1’s

## Slide 20
Procedure
Simplified Boolean Expression
Use K-Map to circle groups of 1’s
1’s may only be circled in powers of 2, starting from largest possible combination and working downward
Write new simplified expression

## Slide 21
Procedure
Logic Circuit Diagram & LabVIEW Simulation
Use new simplified Boolean expression to design a logic circuit (Have TA check/initial work)
Implement circuit using 3 control switches represent input variables and 1 Boolean indicator showing output
Hint:
NOT
AND
OR

## Slide 22
Procedure
NI-ELVIS Prototyping Board
Do NOT electrically connect anything until TA has reviewed your work
Use created logic circuit and IC chip diagram to wire actual circuit on the prototyping board
Be sure to connect each of the ICs to “Ground” and “+5V” (circuit power)
Connect final output to an LED.
**VCC (Voltage at the Common Collector )

## Slide 23
Assignment: Report
Individual Report
Title page
Discussion topics in the manual
Scan in data and lab notes
Original tables and work should be legible
Include screenshots of LabVIEW front and back panels

## Slide 24
Assignment: Presentation
Team presentation
Professional-looking tables
Include screen shots of your programs
  Photo of functioning LED assembly
Explain steps taken to complete lab
  Be prepared to provide walk-through
Include lab data
Refer to “Creating PowerPoint Presentations” found in Online Manual

## Slide 25
Closing
Have all original data signed by TA
Each team member should have turn using software
Submit all work electronically
Return all unused materials to TA