## Slide 1: COMPUTER-AIDED DESIGN (CAD) COMPETITION
EG1003 | LAB 2

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Competition Rules
Assignment
Closing
1
Figure 1: Fusion 360 (left) and Revit (right) icons

## Slide 3: OBJECTIVE
Use CAD software, Fusion 360 and Revit, to visualize a design
Analyze and modify a poorly-designed part in Fusion 360
Enter the modified part in a competition against other redesigns
Design an apartment using Revit
2

## Slide 4: BACKGROUND INFORMATION
Fusion 360
  Introduced in “Introduction to 3D Printing”
  Cloud-based 3D modeling software
  Used for computer-aided design (CAD), computer-aided manufacturing (CAM), renderings, animations, etc.
Figure 2: Fusion 360 in use courtesy of Autodesk
3

## Slide 5: BACKGROUND INFORMATION
Design workspace
  Used to make precisely-scaled drawings of engineering designs
  Sketch a 2D profile
  Generate 3D body using Extrude, Sweep, or Loft
Figure 3: Extrude and Sweep tools
4

## Slide 6: BACKGROUND INFORMATION
Loft
  Creates a 3D extrusion to connect two profiles
Sweep
  Creates a 3D model of a surface (profile) along a specific path
Figure 3: Extrude and Sweep tools
4
Notes: The video has NO AUDIO, so make sure to walk through and narrate what is happening. The first thing they do here is a loft, and then a sweep.

## Slide 7: BACKGROUND INFORMATION
Simulation workspace
  Used to run structural analysis on model under real-world conditions
  Define the constraints (boundary conditions) on the model
  Apply a load to simulate real-world force
  Generate a mesh, an array of polygons making up the body of the model
Figure 4: Fusion 360 mesh courtesy of O’Reilly
5

## Slide 8: BACKGROUND INFORMATION
Simulation workspace
  Run simulation to obtain safety factor, a value used to describe how much stronger a system is than the expected load
  Can determine if an object is ready to sustain real-world loads or needs to be remodified
Figure 5: Fusion 360 simulation courtesy of Engineering.com
6

## Slide 9: BACKGROUND INFORMATION
Revit
  Building modeling software for architects and civil engineers
  Creates homes, buildings, and structural support systems
  Used to create floor, plumbing, electrical, and HVAC plans
Figure 6: Revit in use courtesy of Revit News
7

## Slide 10: MATERIALS
A lab PC
Fusion 360
Revit
Predesigned part files (download directly from the manual)
8
Figure 7: Truss Pyramid

## Slide 11: PROCEDURE
Fusion 360
  Find the load, material, and constraints on the model
  Run a static stress simulation
  Review the initial factor of safety
  Modify the model in the Design workspace within the limits of the competition rules
  Rerun simulations and remodify until the part has safety factor of at least 3
  Save and store the F3D file for later use
9
Figure 8: Screwed bracket static stress simulation

## Slide 12: COMPETITION RULES
Redesigned part must be less than double the initial volume
Redesigned part must have a safety factor of at least 3
Cannot alter the applied loads or constraints
Cannot alter the areas highlighted in red on the model
10
Figure 9: Wire Supported Shelf

## Slide 13: PROCEDURE
Revit
  Create a 350 – 400 square foot apartment for residents/college students
  Contains one of each: bathroom, kitchen, bedroom with bed, table, and desk
  Must have adequate lighting (at least one window) and space
  An electrical plan for the entire apartment
11
Figure 10: Small apartment in Revit courtesy of Balkan Architect

## Slide 14: PROCEDURE
Revit
  Extra credit: Create a 3D rendering and walkthrough video of the apartment
  Submit RVT file to the EG1003 website before the end of lab
12
Figure 11: Small apartment in Revit courtesy of Balkan Architect

## Slide 15: ASSIGNMENT
Submit a RVT file on the EG1003 website
  Due at 11:59 PM the night before Lab 3
Individual lab report:
  Answer discussion questions in manual
  Include screenshots of at least two simulations
  Include screenshots of apartment design
  Due at 11:59 PM the night before Lab 3
13

## Slide 16: ASSIGNMENT
Team presentation:
  Address discussion points in manual
  Include drawings (top, front, most detailed side, isometric) of unmodified and modified part
  Include screenshots of apartment design
  Include 3D rendering and walkthrough video for extra credit
  Due at 11:59 PM the night before Recitation 3
14

## Slide 17: CLOSING
Have all original data signed by a TA
Submit all work electronically
Take screenshots of mechanical part and apartment
Extra credit for 3D rendering and video walkthrough of the Revit apartment
  Must include in the team presentation to get extra credit
15

## Slide 18: QUESTIONS?