## Slide 1: Magnetic Levitation Competition

## Slide 2: Overview
Objective
Background Information
Rules of the Competition
Materials
Procedure
Report / Presentation
Closing

## Slide 3: Objectives
Assemble a cart suspended by magnetic levitation while keeping in mind the aspects of minimal design
Reach Checkpoint A (LED 20) of the track
Reach Checkpoint B (LED 40) of the track

## Slide 4: Magnetic Levitation
1900s: idea of magnetic levitation transportation
1930s: Hermann Kemper developed the basic principle of electromagnetic attraction
Magnetic levitation is a type of levitation that depends on the magnetic fields generated from electromagnets
Types of Magnetic Levitation:
  Electromagnetic Suspension (EMS)
  Electrodynamic Suspension (EDS)

## Slide 5: Electromagnetic Suspension (EMS)
EMS: technique inducing a current through the electromagnets using large power source
Magnetized electromagnets used to create propulsion in the Magnetic Levitation vehicles

## Slide 6: Electrodynamic Suspension (EDS)
EDS: technique of exposing superconductors to magnetic fields that vary with time
Time-varying magnetic fields operate the magnetic levitation vehicles more efficiently

## Slide 7: Earnshaw’s Theorem
Earnshaw’s Theorem states levitation in a magnetic field is not possible
Magnetic field requires additional guidance on the sides of the track for stability (so it doesn’t derail from he track)

## Slide 8: Magnetic Levitation Trains
Three main components: Guidance, Propulsion, Levitation
Propulsion and levitation are caused by electromagnets
Guidance keeps the Magnetic Levitation trains on the track

## Slide 9: Magnetic Levitation Track
Magnetic Levitation track
LEDs and Photo resistors block using provided flag
Power Supply
Electromagnets

## Slide 10: Magnetic Levitation Cart
Prototype of a Magnetic Levitation Cart
Central Magnet Type 2
Outer Magnets
Robot Arms
(Custom)
Flag

## Slide 11: Competition Rules
The TA must approve your design before you are allowed to add your magnetic components.
All the materials you use in your design must be purchased, and are non-refundable.
The maglev cart must fit into the maglev track and must include the flag piece included in the maglev Lego kit.
You may conduct up to three trials and the best ratio of the three trials will be taken.
A TA must be present to oversee your trial or the results of that trial will become invalid.

## Slide 12: Competition Rules
All Magnetic components must be returned at the end of the experiment or your grade for this lab may be jeopardized.
Your 3 trials will be scored this equation…

## Slide 13: Material Price List
Center Magnet Type 1:.………………………$1.00 (only one)
Center Magnet Type 2:.………………………$1.50 (only one)
Outer Magnets (Custom):..…………………………$0.75/each
Long Magnets (3/4” x 3/8” x 1/16’’ thick):…………$0.50/each
Square Magnets (3/8’’ x 3/8’’ x 1/8’’ thick):.………$0.25/each
Bearings: …………………………………………….$0.25/each
Maglev Lego Kit:.…………………………....…$0.00 (only one)

## Slide 14: Procedure
Brainstorm possible designs
Sketch design on paper
Obtain a Maglev Lego Kit after your design is approved by a TA
Assemble your design using the Maglev Lego Kit

## Slide 15: Procedure
Obtain the magnetic parts from a TA
Create price list detailing your design
Conduct practice runs to optimize your design
Conduct your three trials to obtain your minimal design ratio

## Slide 16: Procedure
Disassemble your cart and return all the parts to the Maglev Lego Kit
Magnetic components must be returned before leaving the room

## Slide 17: Assignment: Report
Individual Lab Reports
Title page
Discussion topics in the manual
Include original data with instructor’s initials
Scan in lab notes (ask TA for assistance)
  TA must initial that table and graph were completed
Include table, graph, and photo of container

## Slide 18: Assignment: Presentation
Team presentation
State rules of competition
Describe your design and its concepts
Include table of class results and photo/video of balloon
How could your current design be improved?
Refer to “Creating PowerPoint Presentations” found on EG website

## Slide 19: Closing
Have all original data signed by TA
Submit all work electronically
Clean up workstations
Return all unused materials to TA